## Slide 1
Predict. Print. Break. Compare.
FEA Stress Analysis with SolidWorks 2025
Crescent Valley High School · CTE Engineering

## Slide 2
02
The Big Idea
Students run an FEA simulation, 3D-print the part, physically break it, and compare prediction to reality.
One lesson. Four phases. Real engineering.

## Slide 3
03
Lesson Flow
Phase 1: Learn Sections 1–2 — Physics vocab + FEA workflow
Phase 2: Simulate Sections 3–4 — SolidWorks setup + read results
Phase 3: Build & Test Sections 5–6 — Print specimens + 3-point bend
Phase 4: Analyze Section 7 — Compare, percent error, reflection
Advanced Section 8 — The ABS Trap (differentiation)

## Slide 4
04
What Students Need to Know First
– Six terms: Stress, Strain, Young’s Modulus, Yield Strength, UTS, Factor of Safety
– No physics prerequisite — all taught in Section 1
– The stress-strain curve is the single most important diagram

## Slide 5
05
The Stress-Strain Curve
1 Elastic Proportional, fully recoverable deformation
2 Yield Onset of permanent deformation
3 Plastic Material deforms permanently, strain-hardens
4 Fracture Ultimate failure
Key insight: slope = stiffness, area under curve = toughness

## Slide 6
06
Material Comparison
PLA Stiff, brittle, snaps clean (3,300 MPa bending modulus)
PETG Flexible, tough, stretches before failing (1,900 MPa)
ABS Impact resistant, but worst anisotropy in FDM (2,300 MPa)
Source: CNC Kitchen data

## Slide 7
07
What FEA Actually Does
– Computer breaks part into elements (mesh)
– Solves stress equations at every element
– Assembles full stress picture
The 7-Step Pipeline
1. Geometry
2. Material
3. Fixtures
4. Loads
5. Mesh
6. Solve
7. Interpret

## Slide 8
08
GIGO: The Central Lesson
Garbage In, Garbage Out.
– 6 of 7 steps are HUMAN decisions
– The computer only owns Step 6 (Solve)
– Wrong inputs = precise, beautiful, wrong answers

## Slide 9
09
SolidWorks Setup
– SimulationXpress (free) vs Simulation Standard (paid) — both work
– Custom FDM PLA material profile (E = 3300, Yield = 40, UTS = 50)
– Default library materials are wrong for 3D-printed parts
– Students must create their own material entry

## Slide 10
10
Custom Material Profile — FDM PLA
Property | Value
Young’s Modulus | 3,300 MPa
Yield Strength | 40 MPa
UTS | 50 MPa
Poisson’s Ratio | 0.35
Density | 1,240 kg/m³

## Slide 11
11
Reading Results
– Von Mises stress plot: red = high stress, blue = low
– Displacement plot: how far the part bends (watch for visual exaggeration)
– Factor of Safety: below 1.0 = predicted failure
– Always read the legend numbers, not just the colors

## Slide 12
12
Print Parameters
Printer
Bambu Lab P1S
Slicer Settings
– 100% infill, rectilinear
– 0.20 mm layer height, 4 walls
– 210–215 °C nozzle, 60 °C bed
– Orientation: flat on bed (XY)
Quality Control
– Print ≥ 3 specimens per condition
– Label every specimen
– 24-hour conditioning before testing

## Slide 13
13
Three-Point Bend Test
– Two supports, one load applied at center
– ASTM D790: 16:1 span-to-depth ratio (64 mm span, 4 mm depth)
– Three setup options: dead weight, shop press, CNC Kitchen style
– Safety glasses required for all students

## Slide 14
14
The Formulas
Flexural stress σᶠ = (3 · F · L) / (2 · b · d²)
Flexural modulus Eᶠ = (L³ · m) / (4 · b · d³)
Worked Example
F = 85 N, L = 64 mm, b = 12.7 mm, d = 4 mm
σᶠ = 51.0 MPa within published PLA range

## Slide 15
15
Compare: Predicted vs Actual
Percent Error = | (Predicted – Actual) / Actual | × 100%
< 10% Strong correlation
10 – 20% Acceptable for FDM
20 – 35% Investigate sources of error
> 35% Something fundamentally wrong

## Slide 16
16
Sources of Error
– Material property mismatch
– Print defects (voids, poor layer adhesion)
– Fixture alignment
– Measurement precision (caliper accuracy)
– Isotropic assumption on anisotropic parts
– Temperature and humidity

## Slide 17
17
Advanced: The ABS Trap
– Default SolidWorks ABS = injection-molded properties
– FDM ABS = weaker, highly anisotropic
– Expect 25–50% error with default profile
– Students create corrected FDM ABS profile and see error shrink
Capstone lesson: Assumptions matter more than software.

## Slide 18
18
Differentiation
CORE Sections 1–7 — all juniors
ADVANCED Full Sections 1–8 with ABS investigation
– Self-paced scaffolding on every section page
– Students who miss lecture can work independently

## Slide 19
19
Resources Provided
Live Site mr-mcateer.github.io/fea-solidworks-2025
Binders .docx (CORE + ADVANCED) — copy / paste / modify
Reference Glossary, Formula Sheet, Troubleshooting Guide
Teacher Pacing Guide, Answer Keys, Rubric, Procurement List
Video CNC Kitchen as anchor resource

## Slide 20
20
Assessment
– 100-point rubric + 25 bonus (Section 8)
– Engineering notebook with screenshots, calculations, reflections
– Percent error analysis with identified error sources
– Written prediction BEFORE physical testing

## Slide 21
21
What You Need
Software
– SolidWorks 2025 with SimulationXpress or Simulation Standard
Hardware
– Bambu Lab P1S (or any FDM with enclosure for ABS)
– Basic 3-point bend test rig
– Digital calipers
– Safety glasses
Materials
– PLA filament (required)
– ABS filament (Section 8 only)
Budget
$20 – $58 per class

## Slide 22
22
Next Steps
1 Review the live site: mr-mcateer.github.io/fea-solidworks-2025
2 Pick CORE or ADVANCED path for your classes
3 Modify the .docx binder to fit your schedule
4 Questions → mr-mcateer.github.io/fea-solidworks-2025